## Slide 1
Unless otherwise noted, the content of this course material is licensed under a Creative Commons Attribution 3.0 License. http://creativecommons.org/licenses/by/3.0/
© 2009, Peter Von Buelow
You assume all responsibility for use and potential liability associated with any use of the material. Material contains copyrighted content, used in accordance with U.S. law. Copyright holders of content included in this material should contact open.michigan@umich.edu with any questions, corrections, or clarifications regarding the use of content. The Regents of the University of Michigan do not license the use of third party content posted to this site unless such a license is specifically granted in connection with particular content. Users of content are responsible for their compliance with applicable law. Mention of specific products in this material solely represents the opinion of the speaker and does not represent an endorsement by the University of Michigan. For more information about how to cite these materials visit https://open.umich.edu/education/about/terms-of-use.
Any medical information in this material is intended to inform and educate and is not a tool for self-diagnosis or a replacement for medical evaluation, advice, diagnosis or treatment by a healthcare professional. You should speak to your physician or make an appointment to be seen if you have questions or concerns about this information or your medical condition. Viewer discretion is advised: Material may contain medical images that may be disturbing to some viewers.

## Slide 2
University of Michigan, TCAUP Structures II Slide <number>/26
Architecture 324
Structures II
Reinforced Concrete by
Ultimate Strength Design
LRFD vs. ASD
Failure Modes
Flexure Equations
Analysis of Rectangular Beams
Design of Rectangular Beams
Analysis of Non-rectangular Beams
Design of Non-rectangular Beams
Notes: <number>
PvB

## Slide 3
University of Michigan, TCAUP Structures II Slide <number>/26
Allowable Stress – WSD (ASD)
Actual loads used to determine stress
Allowable stress reduced by factor of safety
Ultimate Strength – (LRFD)
Loads increased depending on type load
 Factors: DL=1.4 LL=1.7 WL=1.3
U=1.4DL+1.7LL
Strength reduced depending on type force
 Factors: flexure=0.9 shear=0.85 column=0.7
Examples:
WSD
Ultimate Strength
Notes: <number>

## Slide 4
University of Michigan, TCAUP Structures II Slide <number>/26
Strength Measurement
Compressive strength
  12”x6” cylinder
  28 day moist cure
  Ultimate (failure) strength
Tensile strength
  12”x6” cylinder
  28 day moist cure
  Ultimate (failure) strength
  Split cylinder test
  Ca. 10% to 20% of f’c
Photos: Source: Xb-70 (wikipedia)
Notes: <number>
Both photos
http://commons.wikimedia.org/wiki/File:Failed_Concrete_Cylinder.jpg
Original uploader was Xb-70 at en.wikipedia
Released into the public domain (by the author).

## Slide 5
University of Michigan, TCAUP Structures II Slide <number>/26
Failure Modes
No Reinforcing
  Brittle failure
Reinforcing < balance
  Steel yields before concrete fails
  ductile failure
Reinforcing = balance
  Concrete fails just as steel yields
Reinforcing > balance
  Concrete fails before steel yields
  Sudden failure
Source: Polyparadigm (wikipedia)
Notes: <number>
http://commons.wikimedia.org/wiki/File:Burst_column.JPG
public domain
(Seismic test column displayed outside UCSD's w:structures laboratory. w:Concrete has burst, exposing w:rebar and w:aggregate (composite). {{PD-user-en|Polyparadigm}})

## Slide 6
University of Michigan, TCAUP Structures II Slide <number>/26
1
1 is a factor to account for the non-linear shape of the compression stress block.
Image Sources: University of Michigan, Department of Architecture
Notes: <number>
GSI Chigozie Ozor

## Slide 7
University of Michigan, TCAUP Structures II Slide <number>/26
Flexure Equations actual ACI equivalent
stress block stress block
Image Sources: University of Michigan, Department of Architecture
Notes: <number>
GSI Chigozie Ozor

## Slide 8
University of Michigan, TCAUP Structures II Slide <number>/26
Balance Condition
From similar triangles at balance condition:
Use equation for a. Substitute into c=a/1
Equate expressions for c:
Image Sources: University of Michigan, Department of Architecture
Notes: <number>
GSI Chigozie Ozor

## Slide 9
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Beam Analysis
Data:
Section dimensions – b, h, d, (span)
Steel area - As
Material properties – f’c, fy
Required:
Strength (of beam) Moment - Mn
Required (by load) Moment – Mu
Load capacity
Find = As/bd
  (check min<  <  max)
Find a
Find Mn
Calculate Mu<= Mn
Determine max. loading (or span)
Image Sources: University of Michigan, Department of Architecture
Notes: <number>
GSI Chigozie Ozor

## Slide 10
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Beam Analysis
Data:
dimensions – b, h, d, (span)
Steel area - As
Material properties – f’c, fy
Required:
Required Moment – Mu
Find = As/bd
  (check min<  <  max)
Notes: <number>
PvB

## Slide 11
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Beam Analysis cont.
Find a
Find Mn
Find Mu
Notes: <number>
PvB

## Slide 12
University of Michigan, TCAUP Structures II Slide <number>/26
Slab Analysis
Data:
Section dimensions – h, span take b = 12”
Steel area - As
Material properties – f’c, fy
Required:
Required Moment – Mu
Maximum LL in PSF
Notes: <number>
PvB

## Slide 13
University of Michigan, TCAUP Structures II Slide <number>/26
Slab Analysis
Find a
Find force T
Find moment arm z
Find strength moment Mn
Notes: <number>
PvB

## Slide 14
University of Michigan, TCAUP Structures II Slide <number>/26
Slab Analysis
Find slab DL
Find Mu
Determine max. loading
Notes: <number>
PvB

## Slide 15
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Beam Design
Data:
Load and Span
Material properties – f’c, fy
All section dimensions – b and h
Required:
Steel area - As
Calculate the dead load and find Mu
d = h – cover – stirrup – db/2 (one layer)
Estimate moment arm jd (or z)  0.9 d and find As
Use As to find a
Use a to find As (repeat…)
Choose bars for As and check  max & min
Check Mu< Mn (final condition)
Design shear reinforcement (stirrups)
Check deflection, crack control, steel development length.
Notes: <number>

## Slide 16
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Slab Design
Data:
Load and Span
Material properties – f’c, fy
Required:
All section dimensions – h
Steel area - As
Calculate the dead load and find Mu
Estimate moment arm jd (or z)  0.9 d and find As
Use As to find a
Use a to find As (repeat…)
Notes: <number>
PvB

## Slide 17
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Slab Design
Use As to find a
Use a to find As (repeat…)
Choose bars for As and check As min & As max
Check Mu< Mn (final condition)
Check deflection, crack control, steel development length.
Notes: <number>
PvB

## Slide 18
University of Michigan, TCAUP Structures II Slide <number>/26
Quiz 9
Can f = Mc/I be used in Ult. Strength concrete beam calculations?
(yes or no)
HINT:
WSD stress Ult. Strength stress
Source: University of Michigan, Department of Architecture
Source: University of Michigan, Department of Architecture
Notes: <number>
GSI Chigozie Ozor

## Slide 19
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Beam Design
Data:
Load and Span
Some section dimensions – b or d
Material properties – f’c, fy
Required:
Steel area - As
Beam dimensions – b or d
Choose (e.g. 0.5  max or 0.18f’c/fy)
Estimate the dead load and find Mu
Calculate bd2
Choose b and solve for d
  b is based on form size – try several to find best
Estimate h and correct weight and Mu
Find As=  bd
Choose bars for As and determine spacing and cover. Recheck h and weight.
Design shear reinforcement (stirrups)
Check deflection, crack control, steel development length.
Notes: <number>

## Slide 20
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Beam Design
Data:
Load and Span
Material properties – f’c, fy
Required:
Steel area - As
Beam dimensions – b and d
Estimate the dead load and find Mu
Choose (e.g. 0.5  max or 0.18f’c/fy)
Notes: <number>

## Slide 21
University of Michigan, TCAUP Structures II Slide <number>/26
Rectangular Beam Design cont
Calculate bd2
Choose b and solve for d
  b is based on form size. try several to find best
Notes: <number>

## Slide 22
University of Michigan, TCAUP Structures II Slide <number>/26
Estimate h and correct weight and Mu
Find As=  bd
Choose bars for As and determine spacing and cover. Recheck h and weight.
Design shear reinforcement (stirrups)
Check deflection, crack control, steel development length.
Rectangular Beam Design
Source: Jack C McCormac, 1978 Design of Reinforced Concrete, Harper and Row, 1978
Notes: <number>
Jack C McCormac,
Design of Reinforced Concrete, 1978
Harper and Row. p.487

## Slide 23
University of Michigan, TCAUP Structures II Slide <number>/26
Non-Rectangular Beam Analysis
Data:
Section dimensions – b, h, d, (span)
Steel area - As
Material properties – f’c, fy
Required:
Required Moment – Mu (or load, or span)
Draw and label diagrams for section and stress
  Determing b effective (for T-beams)
  Locate T and C (or C1 and C2)
Set T=C and write force equations (P=FA)
  T = As fy
  C = 0.85 f’c Ac
Determine the Ac required for C
Working from the top down, add up area to make Ac
Find moment arms (z) for each block of area
Find Mn =  Cz
Find Mu =  Mn  =0.90
Check As min < As < As max
Source: University of Michigan, Department of Architecture
Notes: <number>
GSI Chigozie Ozor

## Slide 24
University of Michigan, TCAUP Structures II Slide <number>/26
Analysis Example
Given: f’c = 3000 psi
fy = 60 ksi
As = 6 in2
Req’d: Capacity, Mu
Find T
Find C in terms of Ac
Set T=C and solve for Ac
Source: University of Michigan, Department of Architecture
Notes: <number>
GSI Chigozie Ozor

## Slide 25
University of Michigan, TCAUP Structures II Slide <number>/26
Example
Draw section and determine areas to make Ac
Solve C for each area in compression.
Notes: <number>

## Slide 26
University of Michigan, TCAUP Structures II Slide <number>/26
Example
Determine moment arms to areas, z.
Calculate Mn by summing the Cz moments.
Find Mu = Mn
Notes: <number>

## Slide 27
University of Michigan, TCAUP Structures II Slide <number>/26
Other Useful Tables:
Image Sources: Jack C McCormac, 1978 Design of Reinforced Concrete, Harper and Row, 1978
Notes: <number>
Jack C McCormac,
Design of Reinforced Concrete, 1978
Harper and Row. pp. 483, 484, 487